## Slide 1
PES University Bengaluru | M.Tech Individual Project — Semester 4
AI-Assisted 3D Assembly Design
Second Review Presentation
Date: 6th June 2026
Abstract
This project develops an end-to-end AI pipeline that analyses partial 3D mechanical assemblies supplied as STEP files, constructs graph representations of parts and their mating relationships, and employs a Graph Attention Network (GAT) to detect missing components. A natural-language assistant (AIDA), powered by Gemini 2.5 Flash, explains assembly structure and suggests corrective actions. The system is delivered as an interactive web application combining a FastAPI backend with a Streamlit frontend.
Presented by
Parthasarathy Perumal

## Slide 2
Detailed Algorithm Design
Graph Neural Network Pipeline for Missing Component Detection
AI-Assisted 3D Assembly Design | PES University Bengaluru
2 / 5
1 Input Processing
→
2 Graph Construction
→
3 GNN Model
→
4 Prediction & Output
▸ STEP file as input
▸ gmsh / OpenCASCADE parser
▸ Extracts 3D solid geometry
▸ Generates mesh & B-rep data
▸ Nodes — 13-dim features:
– Part-type one-hot (8 dims)
– Volume, Surface area
– Bounding-box Δx, Δy, Δz
▸ Edges — 2-dim features:
– Mate-type encoding
– Contact weight
▸ 3-layer Graph Attention Net
▸ Multi-head attention (8 heads)
▸ 64-dim node embeddings
▸ Dropout = 0.1 for regularisation
▸ Adam + ReduceLROnPlateau
▸ MLP Link Predictor
▸ Binary edge score per pair
▸ Threshold → missing parts
▸ NodeRanker for ranking
▸ AIDA (Gemini) explanation
AIDA Assistant:
Gemini 2.5 Flash LLM + engineering_3d_assembly persona → Natural-language explanations, assembly-category analysis, joint-type identification, and corrective suggestions via 6 domain skills.

## Slide 3
Contribution of the Student
Parthasarathy Perumal — Individual Project, M.Tech Sem 4
AI-Assisted 3D Assembly Design | PES University Bengaluru
3 / 5
Core AI / ML Pipeline
▸ Designed & implemented the full STEP-to-GNN pipeline from scratch
▸ Built STEP parser using gmsh + OpenCASCADE — handles real CAD files
▸ Engineered 13-dimensional node feature vectors from 3D geometry
▸ Designed AssemblyGNN: 3-layer GAT with multi-head attention
▸ Implemented MLP Link Predictor for binary missing-part detection
▸ Wrote training loop with Adam, early stopping, ReduceLROnPlateau
▸ Defined evaluation metrics: AUC-ROC and Average Precision (AP)
System, UI & AI Skills Agent
▸ Built FastAPI backend exposing /predict/missing, /explain, /identify, /health
▸ Created Streamlit frontend with Plotly 3D mesh viewer of assemblies
▸ Integrated real-time training monitor within the web dashboard
▸ Developed AIDA agent (Gemini 2.5 Flash) with 6 domain skills YAML
▸ Engineered system prompt / persona (engineering_3d_assembly.yaml)
▸ Wrote shell scripts for one-command service start/stop/log access
▸ Maintained a version-controlled project across macOS (MPS) environment

## Slide 4
Results Obtained — Intermediate
GNN Training Metrics as of May 2026 | Phase 1 Complete
AI-Assisted 3D Assembly Design | PES University Bengaluru
4 / 5
Best AUC-ROC
0.9272
assembly_gnn_20260523 _162431
Avg Precision
0.6463
Current test set AP score
Models Trained
9
Checkpoints saved in trained_models/
Training Runs
6+
Multiple configs explored
Training Configuration
Optimiser
Adam (lr = 1×10⁻³)
LR Scheduler
ReduceLROnPlateau (factor 0.5, patience 10)
Early Stopping
Patience = 20 epochs
Batch strategy
Full-graph (single batch per epoch)
Input features
Node: 13-dim | Edge: 2-dim
Embedding dim
64 (hidden = 128)
Dropout
0.1
Device
MPS (Apple Silicon M-series)
AUC Variation Across Runs
Run 1 (best)
AUC = 0.9272
Optimal LR + data split
Run 2
AUC = 0.8641
Slightly larger dropout
Run 3
AUC = 0.7418
Reduced hidden dim
Run 4
AUC = 0.6367
Latest checkpoint
Run 5
AUC = 0.4424
Current test_metrics.json
Observation
High variance
Sensitivity to data split & LR
Next (Phase 2): Next-component ranking using NodeRanker | Metrics: Hit@K, MRR, NDCG@K | Target AUC ≥ 0.92 consistently

## Slide 5
References
Key Literature, Frameworks, and Tools
AI-Assisted 3D Assembly Design | PES University Bengaluru
5 / 5
[1]
P. Veličković et al. Graph Attention Networks.
ICLR 2018. arXiv:1710.10903
[2]
M. Fey & J. E. Lenssen. Fast Graph Representation Learning with PyTorch Geometric.
ICLR Workshop on Representation Learning on Graphs and Manifolds, 2019.
[3]
Geuzaine, C. & Remacle, J.-F. Gmsh: A 3-D finite element mesh generator with built-in pre- and post-processing facilities.
International Journal for Numerical Methods in Engineering, 79(11), 1309–1331, 2009.
[4]
Open CASCADE Technology (OCCT). Open CASCADE 3D Modeling Kernel.
https://www.opencascade.com (accessed June 2026)
[5]
Google DeepMind. Gemini 2.5 Flash — Multimodal Large Language Model.
Technical Report, Google LLC, 2025.
[6]
FastAPI Framework. Sebastián Ramírez. FastAPI — High Performance, Easy to Learn, Fast to Code.
https://fastapi.tiangolo.com (accessed June 2026)
[7]
Streamlit Inc. Streamlit — A Faster Way to Build and Share Data Apps.
https://streamlit.io (accessed June 2026)
[8]
A. Paszke et al. PyTorch: An Imperative Style, High-Performance Deep Learning Library.
NeurIPS 2019. arXiv:1912.01703